1.

2. Environment
- CLK should have a frequency of 50 MHz with 50% duty cycle
- Reset needs to be asynchronous to the CLK
- create 1 instance of input driver and 4 instances of output driver

3. Input driver
- Check that ACK is asserted for 1 clock cycle only.
- Check that ACK asserts within 4 cycles
- Check if the next packet is only driven after atleast 1 cycles after ACK was asserted

4. Input Driver Packet
1. Wait for reset deassertion
2. Assert BND_PULSE and first packet byte on DATA_IN
3. Deassert BND_PULSE and continue to send packet bytes
4. Assert BND_PULSE for 1 cycle along with the last byte
5. Check if ACK was asserted within 4 cycles of the 2nd assertion of BND_PULSE
6. Check that ACK was asserted for only 1 cycle

5. Output Driver
- Check that the data length(NEWDATA_LEN) is 4, 8, 12, 16
- Check that NEWDATA_LEN is asserted for only 1 cycle
- PROCEED is asserted 1-4 cycles after assertion of NEWDATA_LEN
- PROCEED is asserted for only 1 cycle

6.Output driver packet
1. Wait for NEWDATA_LEN_x assertion
2. Assert PROCEED_x 1-4 cycles after the assertion of NEWDATA_LEN
3. Check if DATA_OUT_x is driven in the next cycle, and the subsequent packets driven 1 per cycle.